## Slide 2: Irish Hauliers Training Pack
Subtitle goes here

## Slide 3
01
Safety Principles – PPE
03
Safety Principles – Tractor unit standards
05
Loading and Unloading
02
Safety Principles – Loose equipment standards
04
Safety Principles – Trailer unit standards

## Slide 4: Safety Principles
Equipment Standards

## Slide 5: Personal Protective Equipment
Personal Protective Equipment
The Seven items of PPE that every driver
should have

## Slide 6: Loose Equipment standards
Transport chains compliant with EN 12195-3.
8mm chains.
  Lashing capacity of 4 tonnes.
  Down-rate to 3 tonnes due to bending
10mm chains.
  Lashing capacity of 6 tonnes.
  Down-rate to 4.5 tonnes due to bending

## Slide 7: Chain failure and wear
Chains always break first where links are bent,
e.g. end hooks, edge of tray, at the hooks on the ‘dog”
Inspect for wear - discard if more than 10% of section damaged or worn
Look for the “key hole effect”
See Technical Information Sheet TIS-0004
Transport Chains & Tensioners
O

## Slide 8: Chain Tensioners
Webbing tensioner for chains
Typical LC 2.5 tonnes
Recently banned
Banned – ‘Sylvester’
O
Turnbuckle or ‘barrel’ type
Typical LC 4 tonnes force
Typical pre-tension 750kgf – 1 tonne
P
O

## Slide 9: Anti Slip matting
Specialised Anti-Slip Matting
  Coefficient = at least 0.60 wet or dry
  3-20 mm thick; about 8-10 mm optimal
  NOT a universal solution - can wear rapidly - inspect before use NEVER USE AS EDGE PROTECTION!! It cuts easily
Conveyor belting
  Harder = Slippery
  Wet - sometimes very slippery
  Typical friction about 0.40
See Technical Information Sheet TIS-0008
Anti-slip matting

## Slide 10: Safety Principles
Tractor and Trailer Standards

## Slide 11: Rotherham Roll Away

## Slide 12: Tractor unit standards

## Slide 13: Tractor unit standards

## Slide 14: Tractor unit standards

## Slide 15: Trailer standards
Saturday 28th August 2010, Scunthorpe, UK
What happened:
  Driver came to collect a loaded trailer
  He dropped his empty trailer and then reversed under the loaded trailer
  Engine was running. Handbrake was NOT applied
  Tractor and trailer rolled away
  Driver tried to get back into the tractor unit to stop it.
  Driver was crushed to death
Learnings
  Standard:
    Handbrake must be applied
    Engine off
    Keys out

## Slide 16: Trailer standards

## Slide 17: Trailer park brakes

## Slide 18: Trailer headboards

## Slide 19: Trailer headboards
Headboards
Check condition
Check specification
EN 12642:2006
Code L: 5 tonnes max load
Code XL: 50% of payload (spread over the face of the headboard)
Loading away from the headboard can generate major impact forces – up to 3 times the weight of the product
Many older trailer headboards are not rated at all

## Slide 20: Trailer stanchion posts and sockets
Varying sizes
  Minimum 80 x 80 x 5mm thick
Condition / corrosion
  Can seriously weaken posts
  Should be inspected / maintained
Must be kept clean and clear of debris!

## Slide 21: Trailer anchor points
Don’t over-load by putting 2 or more lashings to one point
- unless they work in different directions
See Technical Information Sheet TIS-0009
Lashing points

## Slide 22: Trailer lashing points
Some side raves are substantial enough – others are not
< 6mm
Must use edge protection
Attach near a cross member to avoid sliding
Many flat-bed trailers don’t have lashing points

## Slide 23: Loading and Unloading

## Slide 24: What vehicle dangers are there?
Trailer Park
Warehouse Loading Area
Overhead Loading Area
Outside Loading Area

## Slide 25: Loading and Unloading Safety Principles
BE CLEAR – STAY CLEAR
SEE and BE SEEN
You must be aware and look for dangers around you
You must make sure that you are visible to moving vehicles
You must stay clear of moving vehicles, forklifts and loads
How . . .
  Stop and Wait
  Make eye contact with vehicle, crane and forklift drivers
  Seek acknowledgement from vehicle, crane and forklift drivers before moving or approaching
  Keep a safe distance (minimum 2 metres) from vehicles, cranes and forklifts
  Wear High – visibility clothing

## Slide 26: Loading and Unloading Safety Principles

## Slide 27: Loading and Unloading Safety Principles
BE CLEAR and STAY CLEAR
Stay in SAFE ZONES when loading

## Slide 28: BREAK